## Slide 1: Array and Addressing Mode
Chapter 10
Prepared by Shareef Ahmed Tamal Modified(Only Slightly) by Abdus Salam Azad

## Slide 2: One Dimensional Array
  Declaration
  W db 10, 20, 30, 40
Offset Address | Content
0000h | 10
0001h | 20
0002h | 30
0003h | 40

## Slide 3: One Dimensional Array
  Declaration
  W dw 10, 20, 30, 40
Offset Address | Content
0000h | 10
0002h | 20
0004h | 30
0006h | 40

## Slide 4: One Dimensional Array
  Dup operator
  W dw 4 dup (0)
Offset Address | Content
0000h | 0
0002h | 0
0004h | 0
0006h | 0
Repeat count
value

## Slide 5: One Dimensional Array
  Dup operator
  W dw 3, 2, 2 dup (0, 3 dup (1), 5)
  3, 2, 0, 1, 1, 1, 5, 0, 1, 1, 1, 5

## Slide 6: One Dimensional Array
  W dw 3, 2, 5, 8, 1, 6, 8
  Where is the location of 3rd element?
  w + (3-1)*2

## Slide 7: One Dimensional Array
  W dw 3, 2, 5, 8, 1, 6, 8
  Calculate sum of 4th and 6th element
    C : sum = w[3]+w[5]
    Assembly : mov ax, w+6
            add ax, w+10

## Slide 8: One Dimensional Array
  W dw 3, 2, 5, 8, 1, 6, 8
  Calculate sum of all elements
    C : sum=0;
  for(i=0;i<7;i++) sum+=w[i];
    Assembly: ?
      Need a way to iterate over all elements in the array

## Slide 9: Addressing Modes
The way an operand is specified

## Slide 10: So Far we have seen…..
Register Mode:
      When an operand is a register
      Example: Mov Ax, Bx ; src & dest both in register mode
Immediate Mode:
      When an operand is a constant
      Example: Mov Ax, 1
Direct Mode:
      When an operand is a variable
      Example: Mov Ax, C

## Slide 11: There are 4 additional addressing modes
Register Indirect
Based
Indexed
Based Indexed

## Slide 12: Types of Addressing Modes
Register Indirect Mode:
    mov ax, [si]
    The register SI acts as a pointer to a memory location.
    Offset address of the operand is contained in SI register.
200h
SI
AX
Offset Address | Content
0200h | 10
0202h | 20
0204h | 30
0206h | 40
10

## Slide 13: Types of Addressing Modes
Register Indirect Mode:
    BX, SI, DI and BP register can be used to hold offset address.
    For BX, SI and DI, segment number is contained in DS.
    For BP, segment number is contained in ES.

## Slide 14
  W dw 3, 2, 5, 8, 1, 6, 8
  Calculate sum of all elements
W dw 3, 2, 5, 8, 1, 6, 8
Mov ax, @data
Mov ds, ax
Lea SI, W ; SI points to W array
Xor ax,ax ; clear AX
Mov cx, 7
Sum:
  Add ax , [SI]
  Add SI, 2 ; inc SI by 2 bytes/ 1 word as W is an word array
  Loop Sum

## Slide 15: Types of Addressing Modes
Based and Indexed Addressing Mode:
    Operands offset address = displacement + contents in a register
    Displacement can be:
        A variable (Offset address of a variable)
        Constant
        Variable + Offset Address
    Register can be:
        BX, BP, SI, DI
        Segment register rule same as Register Indirect Mode
        If Bx or BP is used, then the mode is called Based
        If SI or DI is used, then called Indexed

## Slide 16: Types of Addressing Modes
Based and Indexed Addressing Mode:
    Syntax of an operand
      [register + displacement]
      [displacement + register]
      [register] + displacement
      displacement + [register]
      Displacement[ register]
    Example:
W dw 3, 2, 5
Mov ax, [W+bx]

## Slide 17: Types of Addressing Modes
Based and Indexed Addressing Mode:
    Syntax of an operand
      [register + displacement]
      [displacement + register]
      [register] + displacement
      displacement + [register]
      Displacement[ register]
    Example:
W dw 3, 2, 5
Mov ax, [W]+bx

## Slide 18: Another Addressing Mode
Based and Indexed Addressing Mode:
    Syntax of an operand
      [register + displacement]
      [displacement + register]
      [register] + displacement
      displacement + [register]
      Displacement[ register]
    Example:
W dw 3, 2, 5
Mov ax, W[bx]

## Slide 19
  W dw 3, 2, 5, 8, 1, 6, 8
  Calculate sum of all elements
W dw 3, 2, 5, 8, 1, 6, 8
Mov ax, @data
Mov ds, ax
Xor ax,ax ; clear AX
Xor bx,bx
Mov cx, 7
Sum:
  Add ax ,W[bx]
  Add bx, 2 ; inc bx by 2 bytes/ 1 word as W is an word array
  Loop Sum

## Slide 20
  W dw 3, 2, 5, 8, 1, 6, 8
  Calculate sum of all elements
W dw 3, 2, 5, 8, 1, 6, 8
Mov ax, @data
Mov ds, ax
Xor ax,ax ; clear AX
Xor bp,bp
Mov cx, 7
Sum:
  Add ax ,W[bp]
  Add bp, 2 ; inc bp by 2 bytes/ 1 word as W is an word array
  Loop Sum
What is the problem with this code?
For bp, SS is the segment register

## Slide 21: 2 Dimensional Array
2 Ways to store 2D array.
  Row Major Order
  Column Major Order
1 | 2 | 3
4 | 5 | 6
Offset | 0000h | 0002h | 0004h | 0006h | 0008h | 000Ah
Content | 1 | 2 | 3 | 4 | 5 | 6
Offset | 0000h | 0002h | 0004h | 0006h | 0008h | 000Ah
Content | 1 | 4 | 2 | 5 | 3 | 6

## Slide 22: 2 Dimensional Array
2 Ways to store 2D array.
  Row Major Order
            W dw 1 ,2, 3
            dw 4, 5, 6
  Column Major Order
            W dw 1 ,4
            dw 2, 5
            dw 3, 6
1 | 2 | 3
4 | 5 | 6

## Slide 23: 2 Dimensional Array
Locating an element
    A is an MxN array
    Locate A[i][j]
    If A stored in row major order then,
        Address of A[i][j] = A + ( (i-1)xN + (j-1) ) x S
    If A stored in column major order then,
        Address of A[i][j] = A + ( (i-1) + (j-1)xM ) x S
    where S=1 if A is byte array and 2 if A is word array

## Slide 24: Based Indexed Addressing Mode
Elements addressed as
      Variable [BX or BP] [SI or DI]
      [BX or BP] + [SI or DI] + variable + constant
      Variable[BX or BP + SI or DI + constant]
      Constant [BX or BP + SI or DI + variable]
Whatever the format, the address is sum of all components
W dw 10, 20, 30, 40, 50 ; bx has 2, SI has 4
Mov ax, w[BX + SI] ; ax = 40
Mov ax, w[BX + SI + 2] ; ax = 50

## Slide 25: PTR Operator
Mov Ax,1 ; Legal
Mov Bh,5 ; Legal
Mov [Bx],1 ; Legal or Illegal?
Mov BYTE PTR [BX],1
Mov WORD PTR [BX],1
Ans: Illegal

## Slide 26: PTR Operator
A db 1
B db 2
Mov ax, A ; Illegal
Mov ax, Word PTR A
2
1
AX
AH
AL

## Slide 27: More
Label pseudo-op
Xlat Instruction